## Slide 1: Review of Aeroacoustic Prediction Techniques for Launch Vehicles
Logan Halstrom
12/1/16

## Slide 2: Motivation
Launch vehicles experience severe acoustic environments
  Launch: engine plumes reflected by pad
  Ascent: Transonic flight, unsteady shocks, engine plume noise
  Abort: Direct abort motor plumb impingement/flow interaction
Potential hazards due to structural vibration
  Failure of electrical or mechanical component
  Fatigue failure of internal or exterior structural component
  Fatigue of payload
Goal: design to minimize acoustics
Need methods of modeling aeroacoustics

## Slide 3: Free-Field Acoustic Testing
Subject test article to unconstrained acoustic source
  Need acoustic source similar to flight
    Blowdown wind tunnel exhaust
    Rocket engine static test

## Slide 4: Reverberant Acoustic Testing
Chamber surrounded by noise-producing horns

## Slide 5: Progressive Wave Test
Chamber connected to outside with many ducts
  Acoustic source outside
  Control source individually in each duct

## Slide 6: Flight Testing
Full-scale flight test with pressure transducers on vehicle
Microphone Phased-Array
  Determine source strength/location accurately from distance

## Slide 7: Wind Tunnel - Ascent
Subscale models in scaled flow
  Modern manufacturing techniques produce high-fidelity models

## Slide 8: Wind Tunnel - Abort
Use heated Helium to simulate rocket motor plumes

## Slide 9: Wind Tunnel - Abort
Complex aeroacoustic effects

## Slide 10: Computational Fluid Dynamics
Can resolve unsteady flow for high-fidelity geometry
  Fraction of cost of wind tunnel
  Not sophisticated enough for aeroacoustics

## Slide 11: Computational Aero-Acoustics
Couple CFD/CAA solvers to produce acoustic results
  LAVA solver (Development still needed)

## Slide 12: Conclusions
All discussed methods are uniquely useful
  Flight test: can’t beat the real thing
  Wind tunnel: much cheaper than flight and still accurate but…
  CFD/CAA: Even cheaper! (but less accurate, needs validation data )
  Acoustic testing: structures must be able to survive vibration
The future
  Computational methods will improve, become more ubiquitous
  Experimental methods will always be required to check computational